## Slide 1: 徐勇志 个人分享 新南威尔士大学 博士 测量工程 北航 硕士 精密仪器及机械 南航 本科 飞行器设计 基于物体检测的室内结构重建 2021-2-28

## Slide 2: Outline
Research problem
Background
Proposed approach: Floor-Det
Proposed approach: Corner-Det
Discussions

## Slide 3: Research problems
Structured modelling
Scan-to-CAD
Floorplan reconstruction
Holistic planar reconstruction
Scan
Floorplan
3D Layout
Still an open problem:
How to capture structural information?
How to recover structural graph?
How to apply to general tasks?

## Slide 4: Applications
GAN
GAN: 1) unaware of building structure or vanishing geometry, introducing various artifacts in close-ups; 2) a user is not able to control what new material or asset to insert.
Structural SLAM
BIM Progress monitoring
Location
compare

## Slide 5: Key challenges
​Arbitrary topology
​Efficient representation and decomposition
​End-to-end learning of structure information: fewer heuristic rules
•​ Instance sensitivity
Fixed topology
Arbitrary topology
Non-parametric reconstruction
longest wall pattern
shortest wall pattern

## Slide 6: Decomposition of graphs
•​ Corner-based: Bottom-up
•​ Region-based: Top-down
•​ Edge-based: under development ?

## Slide 7: Bottom-up approaches
Constraints in integer programming (Gurobi):
Junction degree
Decomposed loop constraint
Opening on wall
Liu, C., Wu, J., Kohli, P., and Furukawa, Y. “Raster-to-vector: revisiting floorplan transformation.” ICCV, 2017.
IP remove spurious junctions and primitives, but cannot recover missed ones.
IP is slow, under 256*256, 2s for Manhattan.
Structure prior only used in IP, not junction detection and region segmentation.
Semantic seg + 11 room types ~= instance seg ? => loop constraint
Classification of junction types is not robust: hallucinate 2 L and one T for each T.

## Slide 8: Bottom-up approaches
N. Nauata, Y. Furukawa, Vectorizing World Buildings: Planar Graph Reconstruction by Primitive Detection and Relationship Inference, ECCV 2020.
Four pixel-wise tasks: (1) corner heatmap, (2) edge semantic seg, (3) region instance seg, (4) region-to-region instance seg
Corner-to-edge: (1) classification of 15 agular bins per corner, (2) used in IP to connect corners.
Region-to-region: (1) semantic mask of common edges, (2) used in IP to encourage edges

## Slide 9: Bottom-up approaches
Optimize the detected primitives by IP to reconstruct topologies.
Four independent models for (1) corner & corner-to-edge, (2) edge, (3) region, (4) region-to-region.
Slow IP: normally 5 mins, 1 hour for complex with 256*256 input.
The representing power of mask-based relationships is weak.
Topology constraints:
1) 1 corner with >=2 edges
2) 1 edge with 2 corners
3) edges not intersect
Region-to-region relationship constraints:
1 edge per r2r instance
Corner-to-edge relationship constraints:
1) connect corners by bins
2) no corner (<0.2), no edge

## Slide 10: Top-down approaches
Neural Procedural Reconstruction for Residential Buildings. Zeng, Wu, and Furukawa. ECCV 2018.
Input: 3D points (incomplete and sparse)
Method: global analysis of entire building structure
5 stages + 7 shape grammar rules

## Slide 11: Top-down approaches
Chen, J., Liu, C., Wu, J., and Furukawa, Y. “Floor-SP: Inverse CAD for Floorplans by Sequential Room-wise Shortest Path.” ICCV 2019.
Network output:
Mask R-CNN output region mask
Dilated Residual Networks (DRN) output corner heatmap
DRN output edge heatmap
How to capture structure info:
Edge semantic mask + room instance mask
Need SP optimization to extract parametric structure

## Slide 12: Top-down approaches
How to recover structure information:
IP can remove spurious corners, but cannot recover missed. Shortest path optimization recovers missed corners. (Dijkstra’s algorithm).
out corners on in corners
out edges on in edges
out edges not on in regions
minimize the number of corners
merging closing corners / edges
Problems:
Primitive detection as normal categories, not improved by structural prior
SP is slow, 5mins for 256*256
Room instance seg suffers from instance sensitivity
8 dominant directions

## Slide 13: Decomposition of structured graphs
Towards real-time and end-to-end structured modeling:
Edge-based decomposition + Object detection
Research gaps between structured modeling and object detection
  Object relationships
  High requirement of localization precision
  ​Instance sensitivity
  ​Unique properties: symmetric, ambiguous direction of axes
(1) Y. Xu, X. Shen, Samsung Lee, Xuesong Li. 3D Object Detection with Deep Neural Networks for Automatic As-built Recons- truction [J]. Journal of Construction Engineering and Management, ASCE. In press .(IF : 2.734, JCR Q1) (2) Y. Xu, X. Shen, Samsung Lee. CorDet : Corner-aware 3D Object Detection Networks for Automated Scan-to-BIM [J]. Journal of Computing in Civil Engineering, ASCE. In press .(IF : 3.46, JCR Q1)
(3) Y. Xu, J. Cheng, X. Shen, Samsung Lee. Floor-Det : Relation-aware object detection network for automatic floorplan re- construction [J]. Automation in Construction, under review .(IF : 5.669, JCR Q1)

## Slide 14: Floor-Det: real-time floorplan reconstruction through relation-aware object detection
real-time and end-to-end
simultaneous sub-tasks: classification, localization, and relation reasoning
simple heuristic post-processing

## Slide 15: RepPoints framework
Z. Yang, S. Liu, H. Hu, L. Wang, S. Lin. RepPoints: Point Set Representation for Object Detection, ICCV 2019.
Box-based representation:
Anchors, proposals, predictions
Coarse locations of objects
Coarse extraction of object features
Point-based representation:
A set of sample points
Automatically arrange RepPoints geometrically (supervised) & indicates semantically significant local areas (un-supervised)
Beneficial for both localization and recognition
Anchor-free
For structural modeling:
Flexible shapes in unified framework
Finer discriminative features for two-stage pipeline
Fusing object-level and local features
Integrate object and structural information

## Slide 16: An end-to-end framework for floorplan reconstruction based on object detection

## Slide 17: Object representations for detecting building primitives
Widely used representation:
(a) (b) (c)
appearance-aware direction;
size-aware direction;
(c) discontinuous sizes and angles when 𝑠𝑥≈𝑠𝑦.
New representation for building objects:
.
ambiguous direction order
symmetric

## Slide 18: Object Refinement using a point-based representation
(a) axis-aligned RoI, (b) rotated RoI, and (c) point-based refinement

## Slide 19: Object Refinement using a point-based representation
Converting representative points into rotated bounding boxes:

## Slide 20: An end-to-end framework for floorplan reconstruction based on object detection
An object detection problem with three auxiliary tasks: 1) detection of room bounding boxes, 2) wall-wall relations, and 3) wall-room relations
Unified framework: walls, windows, and doors
Retrieval of rooms: drifted localization, missed, and redundant walls
Local structural constrain in relationship learning:
is the minimum distance between a point on object-i and a point on object-j,
Training:
, , ,

## Slide 21: An end-to-end framework for floorplan reconstruction based on object detection
NMS:
Corner merging (<0.3 m):
𝒟: distance between two corners,
ℛ: wall-wall relation scores
: corner score
: corner position

## Slide 22: Experiments and validation for Floor-Det

## Slide 23: Experiments and validation for Floor-Det

## Slide 24: Experiments and validation for Floor-Det

## Slide 25: Experiments and validation for Floor-Det

## Slide 26: Experiments and validation for Floor-Det
Two key challenges for the edge-based approach are 1) detection of short edges, 2) precise regression of edge length.
Detections of rooms and wall-room relations: (a), (b) and (e) are room detections of scan-1, -7, and -11; (c) and (d) are wall-room relations of scan-7 and -10, respectively.

## Slide 27: Typical low-quality floorplan reconstruction results
Typical failure cases: 1) too many edges missed, 2) complex structures, 3) small rooms.

## Slide 28: Discussion and limitations
Floor-Det suffers from two key problems: 1) missed and drifted wall-edges, and 2) wall-room relations of rooms with complex shapes.
Future work:
Small object detection
Longest wall instance pattern
Higher input resolution
Precise object localization
A stronger relation learning method: attention mechanism
A unified framework
Currently, two independent models are trained to overcome the large overlap issue between walls and windows.
3D point cloud input

## Slide 29: Discussion and limitations

## Slide 30: CorDet: Corner-aware 3D Object Detection Networks for Automated Scan-to-BIM
Unique properties of building primitives:
Instance sensitivity: boundaries are determinated by corners
Bounding box-shaped
Meaningful local features around corners
Object relationships can be represented based on corners

## Slide 31: CorDet: Corner-aware 3D Object Detection Networks for Automated Scan-to-BIM
Unique properties of building primitives:
Instance sensitivity: boundaries are determinated by corners
Bounding box-shaped
Meaningful local features around corners
Object relationships can be represented based on corners
exactly box-shaped
corners on the background
appearance-aware instance

## Slide 32: CorDet: Corner-aware 3D Object Detection Networks for Automated Scan-to-BIM
Representation of Oriented and Symmetric 3D Objects
, ,
and are irrelevant to the switching of and , but is not. cannot generate a continuous loss function due to the ambiguity between 𝑋_𝑏 and 𝑌_𝑏.
A point-based representation that enables anchor-free object detection:
It is difficult to differentiate between the x- and y-axes through geometric or semantic features
symmetric about both the x- and y-axes
periodicity of rotation angles

## Slide 33: CorDet: Corner-aware 3D Object Detection Networks for Automated Scan-to-BIM
Typical cases of corner sorting by angles: (a) and (b) start from the smallest values; (c) and (d) start from dynamically aligned values.
, : the predicted/ground truth numbers of connected walls on each corner
The consistent order of corners

## Slide 34: CorDet: Corner-aware 3D Object Detection Networks for Automated Scan-to-BIM
Converting four corners to an oriented and symmetric bounding box
(a) predicted corners and middle parameters
(b) parameters of the generated bounding box

## Slide 35: CorDet: Corner-aware 3D Object Detection Networks for Automated Scan-to-BIM
Three stages: (i) initial object detection, (ii) object refinement, and (iii) merging objects with a corner heatmap.

## Slide 36: CorDet: Corner-aware 3D Object Detection Networks for Automated Scan-to-BIM

## Slide 37: CorDet: Corner-aware 3D Object Detection Networks for Automated Scan-to-BIM

## Slide 38: CorDet: Corner-aware 3D Object Detection Networks for Automated Scan-to-BIM

## Slide 39: Object-based structured modeling
Independent object detection:
Armeni，et al., 3d semantic parsing of large-scale indoor spaces, CVPR 2016.
H. Zeng, K. Joseph, A. Vest, Y. Furukawa, Bundle Pooling for Polygonal Architecture Segmentation Problem, CVPR, 2020.
Same as ordinary objects
No relational constraint
Prior-knowledge used for polygonal regression.
Relationships are recovered in post-processing.

## Slide 40: Object-based structured modeling
Y. Xu, W. Xu, D. Cheung, and Z. Tu, Line Segment Detection Using Transformers without Edges, ArXiv210101909 Cs, 2021.
Transformers with multi-scale encoders/decoders
End-to-end pipeline for line segment detection

## Slide 41: Relation-aware structured modeling
Y. Qian, Y. Furukawa. Learning Pairwise Inter-plane Relations for Piecewise Planar Reconstruction. ECCV 2020.
Orientation-CNN:
Input 8-channel img: 3(RGB) + 2(binary mask) + 2(depth maps) + 1(normal product)
Output 3 orientation types: parallel, orthogonal, or neither
Contact-CNN:
Same input
Output 1) touch or not + 2) contact line mask
Same with Floor-Det: get relationships by classification.
Difference: Pipeline and features used for relationship inference.
The relationships can be effectively classified.
Simultaneously seg & relation
Problems to be solved:
Independent segmentation for instances
Inter-plan inconsistencies
Under-segmentation

## Slide 42: 基于图像的室内结构重建
任务：用手机RGB摄像头重建室内3DLayout
方法：单帧透视版HorizonNet
HorizonNet（ICCV19）充分利用先验降低问题纬度：3*1024。
单帧透视版HorizonNet：
对齐输入，Resize为512*512
Binary cross entropy 3*512 +
Linear regression 2*512
Backbone: RNN -> CNN
透视结构数据集生成：Matterport，Panocontext
Fov: 110*90, 82*66
结构分类
直线约束
Backbone: CNN -> Bot
融合SLAM位姿

## Slide 43: 月球车惯性/视觉/天文组合导航
UKF:
EKF:
Y. Xu, X. Ning. A New Method of INS/VNS Integrated Navigation Method for Planetary Exploration Rover [J]. Chinese Journal of Space Science. 2015, 35(6) :721-729. X. Ning, M. Gui, Y. Xu. INS/VNS/CNS integrated navigation method for planetary rovers [J]. Aerospace Science and Tech- nology , 2015, 45 : 102-114. (IF : 4.499, JCR Q1)

## Slide 44: 惯性/视觉动作捕捉算法
磁罗盘标定 当前方法主要是基于椭球拟合，用户难以完成。开发了一个基于椭园拟合的标定方法。
惯性/光学组合动作捕捉 被动式光学捕捉精度高，但存在三个问题：1）抗遮挡能力差，2）Marker ID需要根据刚体形状确定，3）成本高（~正比相机数量）。开发了一种融合IMU和被动光学的定位方案：1) 根据捷联加速度和光学位置匹配关系 + 连续性 + 人体约束 确定Marker ID；2）通过惯性/光学融合提高抗遮挡能力，将8个相机见小到2～4个。

## Slide 45: 谢谢！ 徐勇志